## Slide 1: Circuits

## Slide 2: What do you already know? (electrochemical cell = battery)

## Slide 3: Essential Questions for Circuits
What are the requirements of a circuit?
What is actually going on in a working circuit?
What variable(s) affect what other variable(s) in a circuit? What law(s) and formulas govern the relationship(s) between these variables?
What are the different kinds of circuits? How do they differ?

## Slide 4: Anatomy of a bulb:

## Slide 5: Build a circuit with…
A battery, a bulb, wires
Draw it in your notes, ONCE you figure out how to make the light go on.

## Slide 6: The Requirements of a Circuit

## Slide 7: The Requirements of a Circuit

## Slide 8: The Basic Function of a Circuit

## Slide 9: What is really happening in the circuit?
Go onto Phet, Circuit Construction Kit (DC Only)
Build a circuit with one bulb, one battery, one switch, and as many wires as you need to make the circuit show you clearly what is happening when the switch is closed.
What do the moving balls represent? Which way do they move?
Click the circle in front of Schematic. Sketch the circuit in your notes.

## Slide 10: What is really happening in the circuit?
The balls represent electrons – obviously NOT shown to scale.
The electrons move from negative on the battery, around to positive.
HOWEVER, Current was first defined as the flow of positive charges from the positive terminal to the negative terminal.

## Slide 11: A Useful Analogy
Sometimes, a closed conducting loop (circuit) is compared to a water (amusement) park. Complete this analogy:
Water Park Circuit
pump
electrons
pipes
bulb

## Slide 12: A Useful Analogy
Sometimes, a closed conducting loop (circuit) is compared to a water (amusement) park. Complete this analogy:
Water Park Circuit
pump battery
water electrons
pipes wires
slide/obstacles bulb

## Slide 13: Practice
Answer CYU questions 1 & 2 on PCR Lesson 2b. Put the answers in your daily notes.

## Slide 14: Electric Current
What is it?
What are its units?
How do we measure it?
What variables affect how much current exists in an appliance?

## Slide 15: Electric Current
The flow rate of charges
Unit: ampere (amps, or just A)
1 ampere = 1coulomb of charge flowing thru a conductor in 1 second
Measured with an ammeter
By convention, the “current” flows from positive around to negative.

## Slide 16: What Variable Affects what other Variable(s) in a Circuit?
What is the mathematical relationship between the ______________(_____) through a bulb and the ______________(___) across the bulb in an electrical circuit?

## Slide 17: What is the mathematical relationship between the current(amps) thru one bulb and the potential difference(volts) across the bulb? What is the mathematical relationship between the current(amps) thru two bulbs and the potential difference(volts) across the bulbs?
Now, do the lab again, this time with a real bulb, using real wires, and a “power supply.” What is different when you graph your data? Why do you think it is different?

## Slide 18: And the lab showed…
The electrical current (in amps) thru a bulb is directly proportional to the potential difference (in volts) across the bulb.
What measurement changed when you added a second bulb, and re-did the experiment?

## Slide 19: Resistance
What is it? (use The Lazy Mile at the water park)
What happens in the circuit as the resistance changes?
What is the mathematical relationship between the current(amps) thru a bulb and the resistance(ohms) of the bulb?
What are its units?
How does the PhET simulation show it?

## Slide 20: Ohm’s “Law”: I = DV/R
The current in a circuit element (like a bulb) is directly proportional to the potential difference across the element, and inversely proportional to the resistance of the element

## Slide 21: Measurements in a circuit
I: Current (in amperes (A))
DV: Potential difference (in volts (V))
R: Resistance (in ohms (W))
I = DV/R

## Slide 22: Circuit Schematics

## Slide 23: Example Problem (Ohm’s Law)
Ex: A single loop circuit is made with a 1.5 volt battery, and a light bulb. An ammeter is used to measure a 0.15A current in the loop. What is the resistance of the bulb in this circuit?

## Slide 24: Practice
Complete the 3 practice problems on the WS
Use the PCR if you need extra support.
Use the formula (Ohm’s Law) as a guide to your thinking for #4. It is taken from the PCR lesson 3c (CYU#6)

## Slide 25: Equations
I=DV/R DV = IR R = DV/I
P = I(DV) P=I2R P = (DV)2/R

## Slide 26: Example Problem
Ex: A single loop circuit is made with a 1.5 volt battery, and a light bulb. An ammeter is used to measure a 0.15A current in the loop. What is the resistance of the bulb in this circuit? What power does the battery supply? What power does the bulb dissipate?

## Slide 27: Now Do the Ohm’s Law lab w/ REAL bulbs
What is the mathematical relationship between the current(amps) thru two bulbs and the potential difference(volts) across the bulbs?
How do your results differ from those in the simulation? Why do you think this happened?
What did you notice about the bulbs as the trials proceeded? Why do you think that happened?

## Slide 28: Two Bulb Circuit, cont.
Now leave the battery eliminator set at 4.5V.
Place the ammeter at different positions in the circuit. What do you notice about the value it measures? (Where is the current greater?)
Put the voltmeter across
  The battery eliminator
  Bulb 1
  Bulb 2
  What do you notice?

## Slide 29: Series Circuit

## Slide 30: Series Circuits
All elements in a series circuit have the same current
If you add up the potential differences in the elements that are in series, the result is equal to the potential difference of the battery.
The power supplied by the battery equals the sum of the power dissipated by all resistors.
In Series, Req = R1 + R2 +…+Rn

## Slide 31: Series Circuits…
Charge is neither created nor destroyed, so the __________ is the same for all parts of the circuit.
Energy is neither created nor destroyed, so the sum of the ______________ for all the bulbs must equal the same measurement for the battery.

## Slide 32: The brighter the bulb…
The greater the….

## Slide 33: The brighter the bulb…
The greater the POWER

## Slide 34: Example
Draw a series circuit with a 3.0V battery, a 6W light bulb, and a 3W light bulb. Determine the equivalent resistance of the circuit, the current through the circuit, the potential difference across each item in the circuit, the power supplied by the battery, and the power dissipated (“used”) by each of the bulbs.

## Slide 37: What is a Watt?
A) the unit for energy
B) the unit for current
C) the unit for the rate of energy “used”
D) a measurement of power
E) equal to a joule per second
F) the amount of energy PECO charges about $0.20 for.

## Slide 38: What does the 60 watts mean for a bulb?
A) The bulb has 60 W and after that, it is used up
B) When turned on, the bulb uses 60 watts regardless of the circuit it is in
C) If the bulb is across a potential difference of 120V, the bulb dissipates 60 J of energy each second.

## Slide 39: 60W vs 120W
Determine the resistance of a “60W” bulb and of a “120W” bulb. (they both plug into a 120V outlet)
Which draws more current?

## Slide 40: What is a KILOWATT-HOUR?
A) a unit of power
B) a unit of electricity
C) a unit of energy
D) a unit of work
E) a unit of current
F) a unit of potential difference
G) the amount of heat needed to warm 1.0 ml of water by 1.0°C
H) the amount of heat energy needed to warm 8.6 liters of water by 100°C

## Slide 41: What does that 60W bulb cost…
…. for two hours?

## Slide 42: Save some $$$
A 7W LED provides the same light output as a 13W CFL and as a conventional (incandescent) 60W bulb. If the lamp you wish to use is on for two hours a day, how much will that bulb cost you in one year? (use $0.20 per kWhr, and assume 120V for the outlet potential difference)

## Slide 43: Big Picture cost
 | Incandescent | CFL | LED
Purchase Cost ($) | 0.94 | 1.60 | 5.00
Power (W) | 60 | 13 | 7
Life (hrs) | 1200 | 8000 | 50 000

## Slide 44: A kWhr is….
(1000W) x (1hr)
(1000J/s) x (3600s)
3 600 000J
3.6 x 106J
The amount of energy PECO charges about $0.20 for

## Slide 45: Parallel Circuit

## Slide 46: Parallel Circuits
All elements in a parallel circuit have the same potential difference
If you add up the current in all the elements that are in parallel, the result is equal to the current through the battery.
The power supplied by the battery equals the power dissipated by the resistors in total
In Parallel, 1/Req = 1/R1 + 1/R2 +…+1/Rn

## Slide 47: Electricity Test covers…
Static Electricity: PCR Lessons 1, 2, 3a
Current Electricity: PCR Lessons 2,3,4a&c